Neutrino direction algorithm test using KLG4
- Test criteria:
  - Neutrino flavor: νe
  - Targets: 1H, 12C
  - Energy: 100 MeV ~ 5 GeV
  - Fully contained event condition: < 5 OD hits
  - No fiducial volume cut
  - No nhit cut

---
Angle deviation from true neutrino direction (νe 100 MeV ~ 5 GeV
Target:H1
Target: C12
1σ of cosine distribution

---
100 MeV ~ 1 GeV
Target:H1
Target: C12

---
Reconstructed T2K Event Direction
Events from Ikeda Haruo
Mono-energetic 600 MeV νμ

---
Fiducial volume cut to improve direction fit
Target:H1
Target: C12
R3 vs Energy
Cosine of angle
Radius3 [cm3]

---
R < 650 cm
Target:H1
Target: C12
R3 vs Energy
Cosine of angle
Radius3 [cm3]

---
R < 600 cm
Target:H1
Target: C12
R3 vs Energy
Cosine of angle
Radius3 [cm3]

---
Can we use cosmic ray muon for high energy calibration?
Goal:
PE/cm for muon → PE/MeV
Data selection with KAT Muon Fitter criteria:
- Badness < 20
- Impact parameter < 50 cm
- Runs 5000 ~ 5010
- 204 muon events selected

---
Charge per muon event

---
PMT charge vs angle of PMT position wrt muon track mid-point
μ
PMT
θ
Impact parameter

---
Overlayed all 204 events

---
PMT first hit time vs angle of PMT position wrt muon track mid-point

---
Overlayed all 204 events
PMT prepulsing 30~50 ns before majority of first hits

---
3σ cut wrt average of first hits of neighbor PMTs within 200cm
Fit to 4th order polynomial
Time difference between entry/exit points: Δt = 39.4 ns
Muon speed = 2*8.5m / Δt = 4.3e8 m/s
Unfortunately, faster than light in vacuum by 43%!

---
KLG4 μ stopping power in KamLAND LS
Is it supposed to be this flat?