High Energy Event Imaging and Event Reconstruction
Michinari Sakai
University of Hawaii

---
Motivation
- Want to do event reconstruction for fully contained events.
- We can utilize many photons at high energies to reconstruct event track shape
- Reconstructing lepton track shape and direction gives handle on neutrino direction
- Particle ID

---
Where Are They?
Want high ID total charge and low OD hits (fully contained)
High energy events are here
Sanshiro Enamoto doctoral thesis 2005

---
Algorithm for Event Imaging
Dominikus Hellgartner
(Technische Universität München):
For any given point x in detector volume, calculate:
where
Figure of Merit for point x:
Fit track origin and direction vector to FOM values above some cut.

---
Parameters Used in Algorithm
- Use only 17 inch PMTs.
- Use PMT hit time resolution of 2.4ns (FWHM).
  Should be 3.6ns.
- Index of refraction 1.44
- Muon criteria for rtq events.
- All ID PMT receive hit and OD nhit < 5 for mtq events.

---
Particle ID
1GeV muon
1GeV positron

---
Particle ID
1GeV muon
1GeV positron
Fit ellipsoid and calculate ellipticity
Ellipticity = 0.48
Ellipticity = 0.73

---
Particle ID
1GeV muon
1GeV positron
Calculate length of ellipsoid
Length = 432 cm
Length = 202 cm

---
Lepton Track Angle
Real muon event in KamLAND

---
Lepton Track Angle
Real muon event in KamLAND
But using this much resolution crashes Tohoku computing nodes so we must reduce reconstruction resolution.

---
Lepton Track Angle With Reduced Resolution
Delta angle = 10.9 deg
Delta angle = 170 deg
Delta angle = 15 deg
Delta angle = 5.2 deg
Delta angle = 16 deg
Delta angle = 10.3 deg

---
Lepton Track Angle
Old Result
This Result

---
Lepton Track Angle
Old Result
This Result
Artifact of reconstruction resolution?
Lepton direction sometimes is fitted in reverse.

---
Lepton Track Angle
Old Result
This Result
Angle reconstruction will be further improved by:
- Finer reconstruction resolution.
- Use fully contained events.
- Better lepton direction algorithm.

---
Lepton Direction
Current Algorithm used to fit direction:
- Find Max and Min values of FOM.
- Divide the range between Max and Min values into 3 ranges.
- Get average point of high and mid ranges along track.
- Connect the two points.

---
KamLAND as a Cerenkov Detector
- Discriminate particle ID.
- Fit track length.
- Fit track angle and direction.
- Fully contained events
  = KamLAND can be also utilized as a Cerenkov Detector

---
To Do